## Slide 1: Lecture 15. The Laplace Transform and Operational Calculus
Part (7). Complex Frequency Domain Analysis of Dynamic Circuits

## Slide 2: Systematic Analysis Methods
Welcome to the fifteenth lecture of «The Principle of Circuit».
In our previous lectures on dynamic circuits, we worked exclusively in the time domain.
We solved differential equations directly or used the «Three-Element Method» for simple first-order circuits.
However, what happens when we face a second-order circuit (with both an inductor and a capacitor) or a complex network with multiple loops and nodes?
The Laplace Transform and Operational Calculus

## Slide 3: Systematic Analysis Methods
Solving high-order differential equations becomes extremely difficult and prone to algebraic errors.
Today, we introduce a powerful mathematical tool that simplifies these problems: The Laplace Transform.
The Laplace Transform and Operational Calculus

## Slide 4: Systematic Analysis Methods
This lecture marks the transition from time-domain analysis to the «S-Domain» or «Complex Frequency Domain».
Just as logarithms allow us to turn multiplication into addition, the Laplace Transform allows us to turn calculus (differentiation and integration) into simple algebra (multiplication and division).
The Laplace Transform and Operational Calculus

## Slide 5: Systematic Analysis Methods
Let us define the core concept.
The Laplace Transform is an integral transformation that converts a function of time, , into a function of a complex variable, .
We denote the operation as .
The Laplace Transform and Operational Calculus

## Slide 6: Systematic Analysis Methods
The definition integral is:
The variable is a complex frequency, defined as .
Here, σ (sigma) represents a real growth or decay factor, and ω (omega) represents the angular frequency of oscillation.
Why do we do this?
The Laplace Transform and Operational Calculus

## Slide 7: Systematic Analysis Methods
In the time domain, circuits are described by differential equations.
In the s-domain, these same circuits are described by algebraic polynomial equations.
Solving a polynomial is much easier than solving a differential equation.
Once we solve the algebra in the s-domain, we use the Inverse Laplace Transform to convert the answer back to the time domain.
The Laplace Transform and Operational Calculus

## Slide 8: Systematic Analysis Methods
We do not need to calculate the integral every time.
Instead, we memorize the transforms of the most common signals used in engineering.
Here are the fundamental Transform Pairs:
the Unit Step Function: If (a constant 1 starting at ), ;
the Unit Impulse Function: If , ;
The Laplace Transform and Operational Calculus

## Slide 9: Systematic Analysis Methods
the Exponential Function: If , ; (this is the most common form in circuit analysis);
the Ramp Function: If , .
The Laplace Transform and Operational Calculus

## Slide 10: Systematic Analysis Methods
Now we look at the properties that make this method useful for solving circuits.
The most important property is the Differentiation Property.
Differentiation in time corresponds to multiplication by in the s-domain.
The Laplace Transform and Operational Calculus

## Slide 11: Systematic Analysis Methods
Notice the term . This represents the initial condition.
This is why the Laplace Transform is superior to phasor analysis for transient problems.
Laplace Transform automatically includes the initial conditions (stored energy) in the equation itself.
The Laplace Transform and Operational Calculus

## Slide 12: Systematic Analysis Methods
If the initial condition is zero (), the formula simplifies to:
Similarly, Integration in time corresponds to division by .
The Laplace Transform and Operational Calculus

## Slide 13: Systematic Analysis Methods
We can now apply these properties to our circuit elements: Resistors, Inductors, and Capacitors.
We will create «S-Domain Models» for each component.
The Laplace Transform and Operational Calculus

## Slide 14: Systematic Analysis Methods
1. The Resistor in the S-Domain. Ohm's Law in time is Since R is a constant, the transform is simply:
The resistance remains unchanged in the s-domain.
The Laplace Transform and Operational Calculus

## Slide 15: Systematic Analysis Methods
2. The Inductor in the S-Domain.
The time domain equation is .
Using the differentiation property:
This looks like Ohm's Law () with an extra voltage source.
The term is the «Impedance» of the inductor in the s-domain.
The term is modeled as an independent voltage source in series with the inductor, representing the initial magnetic energy.
The Laplace Transform and Operational Calculus

## Slide 16: Systematic Analysis Methods
3. The Capacitor in the S-Domain. The time domain equation is . Transforming this:
Rearranging to find voltage :
The term is the «Impedance» of the capacitor in the s-domain.
The term is modeled as an independent voltage source in series with the capacitor.
The Laplace Transform and Operational Calculus

## Slide 17: Systematic Analysis Methods
Important Note: The polarity of these initial condition sources must be drawn carefully.
The source opposes the discharge of current.
Now we have a complete method for solving any linear circuit, called Operational Calculus.
The Laplace Transform and Operational Calculus

## Slide 18: Systematic Analysis Methods
The Algorithm of Operational Calculus for Circuit Analysis in the S-Domain:
1. Determine the initial conditions and from the time-domain circuit at .
2. Draw the S-Domain Equivalent Circuit.
replace with impedance and a series source ;
replace with impedance and a series source ;
The Laplace Transform and Operational Calculus

## Slide 19: Systematic Analysis Methods
replace independent sources and with their transforms and (e.g., ).
3. Solve the circuit using standard DC techniques.
You can use Nodal Analysis, Mesh Analysis, Superposition, or Source Transformation.
Treat as just a number or variable in your algebra.
The result will be an equation for the unknown variable, say .
The Laplace Transform and Operational Calculus

## Slide 20: Systematic Analysis Methods
Let's try a conceptual example.
Consider a series R-L circuit connected to a DC voltage at .
Initial current is zero.
The Laplace Transform and Operational Calculus

## Slide 21: Systematic Analysis Methods
Step 1: Initial current .
Step 2: Transform to S-domain.
Source becomes .
Resistor is .
Inductor is impedance (no series source because initial current is 0).
The Laplace Transform and Operational Calculus

## Slide 22: Systematic Analysis Methods
Step 3: Apply KVL (Mesh Analysis), total Voltage = Current Total Impedance:
Solve for Current :
We now have the answer in the S-domain.
The physics is done; now we only have a math problem to return to the time domain.
The Laplace Transform and Operational Calculus

## Slide 23: Systematic Analysis Methods
To return to the time domain, we use the Inverse Laplace Transform.
Usually, our result is a ratio of polynomials, like:
To solve this, we use Partial Fraction Expansion. We break the complex fraction into simpler terms:
The Laplace Transform and Operational Calculus

## Slide 24: Systematic Analysis Methods
The Laplace Transform and Operational Calculus
Do you have any questions at the moment?

## Slide 25: Systematic Analysis Methods
We must calculate the constants A and B (Residues).
Once found, we can write the time domain solution immediately:
The roots of the denominator are called the «Poles» of the system.
The Poles determine the time constants and stability.
If a pole is at , the time decay is .
The location of these poles tells us everything about the speed of the circuit.
The Laplace Transform and Operational Calculus

## Slide 26: Systematic Analysis Methods
Let us finish the R-L example used before. We had:
We perform Partial Fraction Expansion:
The Laplace Transform and Operational Calculus

## Slide 27: Systematic Analysis Methods
Solving for A and B, we find and . So:
Now, apply the Inverse Transform:
The Laplace Transform and Operational Calculus

## Slide 28: Systematic Analysis Methods
This matches exactly the result we derived in Lecture 13 using differential equations.
The Laplace method confirms our previous work but is robust enough to handle much harder problems.
Why is the Laplace Transform so important for engineers?
It is not just for solving circuits.
It is the language of Control Theory and Signal Processing.
The Laplace Transform and Operational Calculus

## Slide 29: Systematic Analysis Methods
Positives of the Laplace Transform:
1. It handles any input.
Whether the source is a sine wave, a step, an impulse, or an exponential, the method is exactly the same.
2. It handles initial conditions automatically.
You do not need to separate the «homogeneous» and «particular» solutions manually.
The Laplace Transform and Operational Calculus

## Slide 30: Systematic Analysis Methods
3. It gives us the Transfer Function .
The Transfer Function is the ratio of Output to Input: .
This function characterizes the circuit completely, independent of what signal is sent into it.
If you know , you know the «DNA» of the circuit.
The Laplace Transform and Operational Calculus

## Slide 31: Systematic Analysis Methods
A major advantage of working in the s-domain is the ability to check the behavior of the circuit at the limits of time without performing the inverse transform.
We use the Initial Value Theorem (IVT) to find the value at .
The Laplace Transform and Operational Calculus

## Slide 32: Systematic Analysis Methods
The Initial Value Theorem allows us to find the value of a time function at zero directly from its s-domain equation.
Mathematically, .
The Laplace Transform and Operational Calculus

## Slide 33: Systematic Analysis Methods
We also use the Final Value Theorem (FVT) to find the steady state at .
The Final Value Theorem enables the calculation of the steady-state value by taking the limit as s approaches zero.
Mathematically, .
These theorems allow for rapid verification of your algebraic derivation.
The Laplace Transform and Operational Calculus

## Slide 34: Systematic Analysis Methods
When we analyze the Transfer Function , the roots of the polynomials provide deep insight into the system.
Poles represent the natural frequencies of the circuit. For example, a pole at corresponds to a decay term .
The location of the poles in the complex plane determines whether the circuit response is stable or unstable.
Engineers plot these on a «Pole-Zero Plot» to visualize the system dynamics.
The Laplace Transform and Operational Calculus

## Slide 35: Systematic Analysis Methods
Stability is the most critical property of any dynamic system.
A stable system is one where the natural response eventually dies out to zero.
In the s-domain, this relates to the real part of the complex frequency σ.
The Laplace Transform and Operational Calculus

## Slide 36: Systematic Analysis Methods
For a circuit to be stable, all poles of its transfer function must lie in the left half of the complex s-plane.
This means the real part of every pole must be negative (σ<0).
If any pole has a positive real part, the time response will grow exponentially and the system is unstable.
An unstable circuit, such as an improperly designed amplifier, will oscillate uncontrollably or saturate.
The Laplace Transform and Operational Calculus

## Slide 37: Systematic Analysis Methods
We can classify s-domain functions into two categories: Driving-Point functions and Transfer functions.
A Driving-Point function relates variables at the same pair of terminals, like the input impedance .
A driving-point impedance relates the voltage and current at the same pair of terminals.
The Laplace Transform and Operational Calculus

## Slide 38: Systematic Analysis Methods
A Transfer Function relates variables at different ports, like the voltage gain .
A transfer function relates an output variable at one port to an input variable at a different port.
Both functions are ratios of polynomials, but only Driving-Point functions must have positive real parts for all passive circuits.
The Laplace Transform and Operational Calculus

## Slide 39: Systematic Analysis Methods
Finally, let us explicitly link the Impulse Response to the Transfer Function.
Recall that the Laplace transform of a unit impulse is simply 1.
If the input to a system is an impulse (), then the output is .
The transfer function of a circuit is mathematically identical to the Laplace transform of its impulse response.
Calculating the inverse Laplace transform of the transfer function yields the impulse response in the time domain.
This is a fundamental concept in testing filters and control systems.
The Laplace Transform and Operational Calculus

## Slide 40: Systematic Analysis Methods
The Laplace Transform and Operational Calculus
Do you have any questions at the moment?

## Slide 41: Systematic Analysis Methods
Thank you for your attention! This concludes our course. It was a pleasure to teaching you.
The Laplace Transform and Operational Calculus