## Slide 1: Lecture 4. Systematic Analysis Methods
Part (2). Analysis of Resistive Circuits

## Slide 2: Systematic Analysis Methods
Systematic Analysis Methods
Welcome back to our course on The Principle of Circuit.
In our previous lectures, we established the fundamental behavior of ideal elements and explored how to simplify circuits using equivalent transformations, such as series, parallel, and Delta-Star conversions.
However, not all circuits can be simplified using these basic reduction techniques.
When we encounter complex networks with multiple sources and interconnections that are neither series nor parallel, we require more powerful mathematical tools.

## Slide 3: Systematic Analysis Methods
Systematic Analysis Methods
But first of all, let’s review the example of Y-Δ transform because it is not so obvious to understand

## Slide 4: Systematic Analysis Methods
Systematic Analysis Methods
So, we can designate the resistors AC, BC and AB at the Δ-circuit and az, bz and cz at the Y-circuit to make the formulas look more geometric, now we are talking about resistors between two points.
These formulas can be written as on the slide

## Slide 5: Systematic Analysis Methods
Systematic Analysis Methods
Let’s apply these formulas to transform Δ to Y circuit

## Slide 6: Systematic Analysis Methods
Systematic Analysis Methods
Therefore, we will have the new Y-circuit, equivalent to the Δ one

## Slide 7: Systematic Analysis Methods
Systematic Analysis Methods
And now let’s try an Y-Δ transform

## Slide 8: Systematic Analysis Methods
Systematic Analysis Methods
Therefore, we will have the new Δ-circuit, equivalent to the Y one

## Slide 9: Systematic Analysis Methods
Systematic Analysis Methods
Equivalent transform means, that if you change Δ-shaped part in a circuit to calculated equivalent Y-shaped part nothing will changes in this circuit
Voltages and currents must be stable

## Slide 10: Systematic Analysis Methods
Systematic Analysis Methods
You can see that current doesn’t change after transformation here

## Slide 11: Systematic Analysis Methods
Systematic Analysis Methods
And here

## Slide 12: Systematic Analysis Methods
Systematic Analysis Methods
Now we can go next.
Today, we begin the study of systematic analysis methods.
These are algorithmic procedures that allow us to convert any linear circuit into a system of simultaneous algebraic equations.
The primary objective of this lecture is to master the Branch Current Method, the Nodal Voltage Method, and the Mesh Current Method.
These three techniques form the toolkit of every professional electrical engineer.

## Slide 13: Systematic Analysis Methods
Systematic Analysis Methods
Systematic analysis methods provide a structured step-by-step approach to writing exactly enough independent equations to solve the circuit.
We will trade the visual intuition of circuit reduction for the mathematical rigor of linear algebra.
While circuit reduction changes the structure of the circuit to find a single value, systematic methods leave the circuit structure intact and solve for all variables simultaneously.

## Slide 14: Systematic Analysis Methods
Systematic Analysis Methods
To understand why we need these methods, consider a circuit with two voltage sources and three resistors arranged in two loops.
We know Kirchhoff's Laws hold true: the sum of currents at any node is zero (KCL) and the sum of voltages in any loop is zero (KVL).
If we apply these laws randomly, we might end up with more equations than variables, or equations that are redundant. Systematic analysis methods provide a structured step-by-step approach to writing exactly enough independent equations to solve the circuit.

## Slide 15: Systematic Analysis Methods
Systematic Analysis Methods
We will trade the visual intuition of circuit reduction for the mathematical rigor of linear algebra.
While circuit reduction changes the structure of the circuit to find a single value, systematic methods leave the circuit structure intact and solve for all variables simultaneously.

## Slide 16: Systematic Analysis Methods
Systematic Analysis Methods
Before we proceed, we must strictly define our topological terminology. As we defined in Lecture 2:
a Node is a connection point between two or more elements;
a Branch is a path containing a single element connecting two nodes;
a Loop is any closed path through the circuit.
To these, we add a specific type of loop called a «Mesh».

## Slide 17: Systematic Analysis Methods
A Mesh is a loop that does not contain any other loops within it.
You can think of a mesh as a «window pane» in the circuit diagram. In Fig. here you can see that sum of all meshes can be named «loop».
Systematic Analysis Methods

## Slide 18: Systematic Analysis Methods
The number of independent equations required to solve a circuit is determined by its topology.
If a circuit has n nodes and b branches, we need a specific number of KCL and KVL equations to find every current and voltage.
Systematic Analysis Methods

## Slide 19: Systematic Analysis Methods
The first and most fundamental method is the Branch Current Method. This method is the most direct application of Kirchhoff's laws.
In this method, we treat the current flowing through each branch as an unknown variable. If a circuit has branches, we will have unknown currents (). To solve for these unknowns, we must write a system of independent equations.
Systematic Analysis Methods

## Slide 20: Systematic Analysis Methods
The Branch Current Method is universally applicable to any circuit, but it is computationally inefficient.
For a circuit with just 5 branches, you must solve a system of 5 simultaneous equations.
While this is easy for a computer, it is boring for a human.
However, understanding this method is crucial because it proves that KCL and KVL are sufficient to solve any network.
Systematic Analysis Methods

## Slide 21: Systematic Analysis Methods
The algorithm for the Branch Current Method:
arbitrarily assign a reference direction (current arrow) for each branch current; Remember, if the calculated value is negative, the actual direction is opposite;
count the number of nodes (n). Write KCL equations for ; We omit one node because its equation is mathematically dependent on the others (redundant);
Systematic Analysis Methods

## Slide 22: Systematic Analysis Methods
count the number of independent loops (meshes). Write KVL equations for these loops;
solve the resulting system of linear equations to determine the individual branch currents.
Systematic Analysis Methods

## Slide 23: Systematic Analysis Methods
It is imperative to follow the passive sign convention when writing the KVL equations: voltage drops across resistors are positive in the direction of the current (), and voltage rises are negative.
Systematic Analysis Methods

## Slide 24: Systematic Analysis Methods
Let us apply this to a practical example. Imagine a circuit with two generic meshes: a left loop and a right loop, sharing a central vertical resistor. Let us say we have 3 branches. We label the currents , and . We have 2 nodes (top and bottom).
Systematic Analysis Methods

## Slide 25: Systematic Analysis Methods
We write KCL for the top node:
Sum of currents entering equals sum of currents leaving:
We have 2 meshes.
We write KVL for the left mesh and the right mesh.
This gives us 3 equations for our 3 unknown currents.
Once the branch currents are known, we can calculate any voltage using Ohm’s Law and any power using .
Systematic Analysis Methods

## Slide 26: Systematic Analysis Methods
Let’s look at two examples that fit that problem.
First, let’s consider a circuit similar to Fig. Let the voltage of the sources be the same and amount to 9 V.
Systematic Analysis Methods

## Slide 27: Systematic Analysis Methods
In this case, and .
The system of equations:
Substituting the values ( ):
Systematic Analysis Methods

## Slide 28: Systematic Analysis Methods
The symmetry of the circuit and sources means . Substituting for in the first equation:
Current | Value (A)
𝑖1 (Left Mesh Current) | 0.9 A
𝑖2 (Right Mesh Current) | 0.9 A
𝑖(100 Ω) (Center Branch Current) | 𝑖1−𝑖2=0 𝐴
Systematic Analysis Methods

## Slide 29: Systematic Analysis Methods
Second, let’s consider a different circuit with one source only.
In this case, the source in the left mesh is V=9 V, and the source in the right mesh is 0 V.
Systematic Analysis Methods

## Slide 30: Systematic Analysis Methods
The system of equations (from Section 2.A) was:
Substituting the values ():
From equation (5'):
Systematic Analysis Methods

## Slide 31: Systematic Analysis Methods
Substitute into equation (4'):
Now find :
Systematic Analysis Methods

## Slide 32: Systematic Analysis Methods
Here are all results in one table.
Current | Value (A)
𝑖1 (Left Mesh Current) | 9⋅(1.3)/43≈0.2721 𝐴
𝑖2 (Right Mesh Current) | 9/43≈0.2093 𝐴
𝑖(100 Ω) (Center Branch Current) | 𝑖1 −𝑖2 =0.0628 𝐴
Systematic Analysis Methods

## Slide 33: Systematic Analysis Methods
Systematic Analysis Methods
Do you have you any questions at the moment?

## Slide 34: Systematic Analysis Methods
As you can see, the Branch Current Method generates a large number of equations. Engineers prefer efficiency. We want to solve for fewer variables. This leads us to The Nodal Voltage Method
It reduces the number of equations by solving for «Node Voltages» instead of currents.
Recall from Lecture 1 that electric potential is the voltage at a specific point with respect to a common reference point (Ground).
Systematic Analysis Methods

## Slide 35: Systematic Analysis Methods
In this method, the unknown variables are the potentials of the essential nodes () relative to a chosen reference node (0 V).
If a circuit has n nodes, we only need to solve (n-1) equations. This is often much faster than finding all branch currents.
The Nodal Voltage Method is based on Kirchhoff’s Current Law (KCL).
For every non-reference node, we write an equation stating that the algebraic sum of currents leaving the node is zero.
Systematic Analysis Methods

## Slide 36: Systematic Analysis Methods
But how do we write currents in terms of node voltages?
We use Ohm's Law.
Consider a resistor R connecting Node A (potential ) and Node B (potential ).
The current flows from higher potential to lower potential.
Systematic Analysis Methods

## Slide 37: Systematic Analysis Methods
The current flowing from to is defined as the difference in potential divided by the resistance:
This is the fundamental equation of Nodal Analysis.
It combines Ohm's Law and KCL into a single step.
Systematic Analysis Methods

## Slide 38: Systematic Analysis Methods
We follow this systematic Algorithm for Nodal Analysis:
select a Reference Node (Ground). Usually, we choose the node with the most connections or the negative terminal of the main source. label its potential as V;
label the potentials of the remaining nodes as variables .
Systematic Analysis Methods

## Slide 39: Systematic Analysis Methods
write a KCL equation for each non-reference node. Express every branch current as
Systematic Analysis Methods

## Slide 40: Systematic Analysis Methods
if a current leaves the node, treat it as positive.
If a current enters the node (from a source), treat it as negative;
solve the system of equations to find the node voltages.
Once the node voltages are known, the branch currents can be easily calculated using the equation .
Systematic Analysis Methods

## Slide 41: Systematic Analysis Methods
Let us look at a specific case involving current sources.
Nodal analysis is extremely powerful when the circuit contains independent current sources.
Because a current source forces a known value into the node, we do not need to use the v/R term for that branch;
Systematic Analysis Methods

## Slide 42: Systematic Analysis Methods
We simply substitute the known source current value directly into the KCL equation.
For example, if a 5A source pumps current into Node 1, the KCL equation simply includes a «-5» term (negative because it enters).
If the circuit contains only current sources and resistors, the Nodal equations can be written by inspection using the conductance matrix.
Systematic Analysis Methods

## Slide 43: Systematic Analysis Methods
What if we have voltage sources?
If a voltage source is connected between the reference node and a non-reference node, the analysis is even easier.
The voltage of that node is simply equal to the source voltage.
We do not need to write an equation for it; the variable is already known.
Systematic Analysis Methods

## Slide 44: Systematic Analysis Methods
However, if an ideal voltage source is connected between two non-reference nodes, we use the concept of a Supernode.
A Supernode is formed by enclosing the voltage source and its two connecting nodes inside a boundary.
We treat this entire boundary as a single point and apply KCL to it.
Systematic Analysis Methods

## Slide 45: Systematic Analysis Methods
We need one auxiliary equation: the difference between the two node voltages inside the supernode equals the source voltage ().
Systematic Analysis Methods

## Slide 46: Systematic Analysis Methods
Now we turn to the third method, which is the counterpart to Nodal Analysis – the Mesh Current Method (Mesh Analysis)
While Nodal Analysis relies on KCL and node voltages, Mesh Analysis relies on Kirchhoff’s Voltage Law (KVL) and «Mesh Currents».
This method is generally preferred when a circuit contains many voltage sources and series connections.
Systematic Analysis Methods

## Slide 47: Systematic Analysis Methods
A mesh current is a hypothetical current that flows around a closed loop (mesh).
Unlike branch currents, which are physically measurable, mesh currents are a mathematical abstraction.
The physical current in a branch is the algebraic sum of the mesh currents flowing through it.
Let us visualize the mesh current. Imagine each mesh is a separate gear rotating clockwise. In a branch that is shared by two meshes, two «gears» touch.
Systematic Analysis Methods

## Slide 48: Systematic Analysis Methods
If mesh current goes down through a shared resistor and mesh current goes up through the same resistor, the actual physical current is the difference:
Systematic Analysis Methods

## Slide 49: Systematic Analysis Methods
The Mesh Current Method algorithm is as follows:
identify all elementary meshes (loops without inner loops);
assign a mesh current variable () to each mesh. By convention, we usually define all mesh currents to flow clockwise. This standardizes our equations;
write a KVL equation for each mesh. Sum the voltage drops around the loop to zero;
solve the linear equations to find the mesh currents.
Systematic Analysis Methods

## Slide 50: Systematic Analysis Methods
When writing the KVL equation for a specific mesh (let's call it Mesh 1), we encounter two types of voltage drops across resistors:
unshared Resistors – the voltage drop is simply the resistor value times the mesh current ();
Systematic Analysis Methods

## Slide 51: Systematic Analysis Methods
shared Resistors – for a resistor shared between Mesh 1 and Mesh 2, the current flowing through it is (assuming clockwise direction), therefore, the voltage drop is .
Systematic Analysis Methods

## Slide 52: Systematic Analysis Methods
The general pattern for the KVL equation of Mesh 1 is:
This «Self-Resistance minus Mutual-Resistance» pattern makes it very easy to check your work for errors.
.
Systematic Analysis Methods

## Slide 53: Systematic Analysis Methods
Let's illustrate the concept of shared resistance and mesh currents.
Imagine two loops of water pipes sharing a common wall.
The water in the left loop circulates clockwise.
The water in the right loop also circulates clockwise.
Systematic Analysis Methods

## Slide 54: Systematic Analysis Methods

## Slide 55: Systematic Analysis Methods
At the common wall (the shared branch), the left water pushes down, and the right water pushes up.
The net flow of water in the central pipe is the subtraction of the two flows.
If the left flow is stronger, the water goes down.
If the right flow is stronger, it goes up.
In our equations, we account for this by writing the voltage drop as .
Systematic Analysis Methods

## Slide 56: Systematic Analysis Methods
Just as current sources simplified Nodal Analysis, Voltage Sources simplify Mesh Analysis. If a branch contains a voltage source, it simply adds a constant term to the KVL equation.
However, if a Current Source exists in a branch shared by two meshes, we have a problem: we cannot define the voltage drop across an ideal current source directly.
In this case, we use the concept of a Supermesh.
Systematic Analysis Methods

## Slide 57: Systematic Analysis Methods
A Supermesh is created by conceptually removing the current source branch and writing a KVL equation around the larger combined loop.
We also write a constraint equation: the difference between the two mesh currents must equal the value of the current source ().
Systematic Analysis Methods

## Slide 58: Systematic Analysis Methods
But which of these methods should you choose? Professional engineers choose the method that results in the fewest equations.
Count the Nodes (n) and Meshes (m):
if use Nodal Analysis (this is usually true for parallel circuits or circuits with many current sources);
if– use Mesh Analysis (this is usually true for series-heavy circuits or circuits with many voltage sources).
Systematic Analysis Methods

## Slide 59: Systematic Analysis Methods
Example: a bridge circuit has 4 nodes and 3 meshes.
Nodal Analysis requires 4-1=3 equations.
Mesh Analysis requires 3 equations.
They are equal in difficulty.
However, if we ground the bottom node,
Nodal might feel more intuitive for finding voltages.
Systematic Analysis Methods

## Slide 60: Systematic Analysis Methods
Let us practice with a quick thought experiment. Imagine a circuit with 10 parallel resistors and one voltage source.
Systematic Analysis Methods

## Slide 61: Systematic Analysis Methods
Number of Meshes – 10 (you would need to solve a 10×10 matrix). Number of Essential Nodes – 2 (top wire and bottom wire).
Systematic Analysis Methods

## Slide 62: Systematic Analysis Methods
Using Nodal Analysis, you solve one equation. Using Mesh Analysis, you solve ten.
Choosing the correct systematic method saves you hours of work.
Systematic Analysis Methods

## Slide 63: Systematic Analysis Methods
In summary of this lecture, we have moved from ad-hoc analysis to rigorous algorithms:
the Branch Current Method uses fundamental KCL/KVL but generates many variables;
the Nodal Voltage Method is best for finding voltages and works well with current sources. It is based on KCL;
the Mesh Current Method is best for finding loop currents and works well with voltage sources. It is based on KVL.
Systematic Analysis Methods

## Slide 64: Systematic Analysis Methods
Mastery of these three methods is the «literacy» of circuit theory.
You cannot proceed to complex electronics, AC analysis, or power systems without them. In the next lecture, we will explore Fundamental Circuit Theorems like Superposition and Thevenin’s Theorem, which allow us to break complex circuits into simpler pieces.
Systematic Analysis Methods

## Slide 65: Systematic Analysis Methods
Systematic Analysis Methods
Thank you for your attention!
Do you have you any questions?